## Slide 1: n_TOF Data
Nikolay Sosnin 26Al Filtering 31 July 2023
α/p/t/γ…
Source
Detector

## Slide 2: n_TOF Data
Nikolay Sosnin 26Al Filtering 31 July 2023
α/p/t/γ…
Source
Detector
Time
Voltage

## Slide 3: n_TOF Data
Nikolay Sosnin 26Al Filtering 31 July 2023
α/p/t/γ…
Source
Detector
Time
Voltage
Analog-to-Digital converter (ADC)
in data acquisition (DAQ)

## Slide 4: n_TOF Data
Nikolay Sosnin 26Al Filtering 31 July 2023
α/p/t/γ…
Source
Detector
Time
Voltage
Analog-to-Digital converter (ADC) cards
in data acquisition (DAQ)
computers
CERN tape server

## Slide 5: n_TOF Data
Nikolay Sosnin 26Al Filtering 31 July 2023
Pick-up detector senses current induced in beamline by protons and sends signal to DAQ that protons arrive imminently.
DAQ starts saving output of detectors for 120 milliseconds
Protons
Lead
Pick-up (PKUP)
Trigger to write data

## Slide 6: n_TOF Data
Nikolay Sosnin 26Al Filtering 31 July 2023
Pick-up detector senses current induced in beamline by protons and sends signal to DAQ that protons arrive imminently.
DAQ starts saving output of detectors for 120 milliseconds
Protons
Lead
Neutrons
Detectors
in EAR2
Detectors
in EAR1
Pick-up (PKUP)
Trigger to write data

## Slide 7: n_TOF Data
Nikolay Sosnin 26Al Filtering 31 July 2023
Pick-up detector senses current induced in beamline by protons and sends signal to DAQ that protons arrive imminently.
DAQ starts saving output of detectors for 120 milliseconds
ADC has a certain range (e.g. 14-bit, i.e. 214 = 16384 channels into which signal amplitude is divided)
ADC has a certain rate (e.g. 125 mega-samples/second, i.e. signal is written 125e6 times per second = 8 ns / sample)
Protons
Lead
Neutrons
Detectors
in EAR2
Detectors
in EAR1
Pick-up (PKUP)
Trigger to write data
Signals

## Slide 8: Staging
Nikolay Sosnin 26Al Filtering 31 July 2023
Data saved on tape server can be re-accessed through two steps:
Staging: converting magnetic tape back to digital data (takes a few days) stored on computer cluster LXPLUS
raw2root: C++ based code, which converts digital output of tape server to ROOT histograms for analysis
Time
Voltage
Staging + raw2root
CERN tape server

## Slide 9: raw2root
Nikolay Sosnin 26Al Filtering 31 July 2023
raw2root is composed of two main components
ntoflib, custom n_TOF analysis libraries
detector class, user-written routine
In detector class, user specifies how the signal trace should be handled (filtering) and what parameters are saved to raw2root output
raw2root
ntoflib
Detector
class
UserInput
Desired output, e.g. amplitudes, times of signals

## Slide 10: MWD detector class
Nikolay Sosnin 26Al Filtering 31 July 2023
Edinburgh group have a custom detector class for raw2root, called MWDdetector.cc
The code applies a series of digital filters to data to efficiently extract signal times and amplitudes
Filters:
Moving Average
Single-pole low- and high-pass filters
Differentiator
Moving Window Deconvolution (MWD)
Digital filtering compendium:
http://www.dspguide.com/pdfbook.htm

## Slide 11: Moving Average (MA)
Nikolay Sosnin 26Al Filtering 31 July 2023
A window of fixed width moves through signal trace time channel by time channel.
Averages all the data points within a window
Results in a smoother pulse with less high-frequency noise, which gets averaged out between channels
Window size is best set to noise risetime in channels as a first guess (careful that it's not the identical to signal risetime, or things get tough)
Original
After moving average
Pulses offset vertically for visibility

## Slide 12: Low- and high-pass filters
Nikolay Sosnin 26Al Filtering 31 July 2023
Digital filters have transfer functions, which define filter response to inputs at a given signal frequency (think Fourier analysis, converting amplitudes to frequencies of waves added to put together a given signal shape)
Poles and zeroes of a transfer function define which frequencies get amplified and which zeroed
Low- and high-pass filters define an upper and a lower boundary on frequencies that are transferred to filter output
Can cut out specific noise (e.g. 50-60 Hz oscillations from poor grounding, MHz oscillations from unshielded cable) as a result
Original
After low-pass
After high-pass

## Slide 13: Differentiator
Nikolay Sosnin 26Al Filtering 31 July 2023
Takes the slope over a certain dT window of the high- and low-pass filtered trace
When derivative passes over a real signal, it will increase above baseline, then drop below baseline
Zero-crossing identifies signal time
This corresponds to a consistent fraction of signal amplitude for a properly-chosen window size
First-guess window size = signal risetime
Original
Derivative
Zoom

## Slide 14: Moving Window Deconvolution
Nikolay Sosnin 26Al Filtering 31 July 2023
Jordanov and Knoll, NIM A 345 (1994), 337-345 (not original paper, but best explanation)
Compensates for ballistic deficit (loss of signal during pre-amp charge collection time due to pre-amp continuously discharging as signal is collected)
Several parameters: timing constant μ (the decay time of pre-amp provided by manufacturer), windows m and l (m = moving window size, should be at least equal to full risetime of a signal, l = flat-top width)
Produces trapezoidal output (so if flat-top width = 0, the output is a triangle)
Allows clean amplitude extraction
If μ is set incorrectly, the pulse does not return to baseline (under- or over-shoot)
Original
MWD+MA
MWD

## Slide 15: Baseline estimation (not a filter, but important at n_TOF)
Nikolay Sosnin 26Al Filtering 31 July 2023
After gamma-flash, there can be long undershoot in baseline
MWDdetector class uses three segments of baseline before a signal candidate, averaging the signal there
Lowest of the three is chosen as "true" baseline

## Slide 16: Summary
Nikolay Sosnin 26Al Filtering 31 July 2023
raw trace
2x MA
high-pass
low-pass
Differentiator
Signal time
MWD
MA
Amplitude
Baseline
The dreadful gamma flash
Mission: get signals here
Pulser